## Slide 1
Ingmar Poese
27/03/2023
Cascading ALTO
IETF-116

## Slide 2
About BENOCS
Location: Berlin, Germany
Industry: Telecommunications, Network Telemetry
Mission: To improve network traffic conditions and visibility
2013
Founded as a Spin-off of Deutsche Telekom
2015
First live customers for BENOCS Director
2018
Fully developed BENOCS Analytics enters the market
2020
Customer base expanded globally
Notes: <number>

## Slide 3
CE (Core Engine) Architecture
General Architecture Gather Information
  Primarily from control plane
    IGP (IS-IS, OPSFv2/3)
    BGP (RR-connection to all border routers)
    Augment Information (SNMP, (streaming) telemetry, Inventory, propriatory...)
  Convert deployment specific information/configuration into an internal, standardized format
    Prefixmatch → match a prefix to originate from a specific router
    Pathcache → use IGP to calculate path throught the network
Building an ALTO map based on this information depends on the ingress point
FROM:
Steering Hyper-Giants’ Traffic at Scale, Pujol et. al., CoNext’19

## Slide 4
Challenge 1: Ingress Point
Definition Determine where traffic from an IP/subnet enters the network
Easy
Traffic enters via caches/PNI. No path asymmetrical path, no middle party(s), bi-lateral relationship
  This is the majority of the traffic
Hard
Traffic enters via Peering.
  IGP/BGP cannot be used
    Inference statistically via Dataplane
  Compute/Data heavy operation
  Needs to always be up to date
  “Small” amount of overflow can have severe impact
Dissecting Apple’s Meta-CDN during an ios Update, Blending et al., IMC’18

## Slide 5
Challenge 2: Cascasing Path optimization
Multi Tier ASN Setup
  Larger networks run mutiple ASNs.
    Can be private or offical ASNs
    One company or conglomerate of companies
  HG/CDN caches are usually deployed in the parent ASN
    Ingress Point issues resurface
Unpublished: currently under submission
Unpublished: currently under submission

## Slide 6
Solution: Multi-domain ALTO
Multi-Domain ALTO to the rescue
  Partial path information from different ASNs along the AS path builds a full overview
    AS-State map made up if link-state protocol networks ?
  Individual, inaccurate(?), data-heavy operations can be ceased
    ALTO now supplies the information
  ALTO can solve this issue by supplying Maps for each individual network
    One (replicated) Meta-ALTO collects the maps and builds a full overview (DNS like ?)
    Each local ALTO pulls information from all other ALTO individually.